## Slide 1: Bootloader
Presented by Group 2 !

## Slide 2: TEAM MEMBERS
Nguyen Duc Tung
Tran Dinh Bien
Member
Presenter
Slideguy
Code
Team Leader
Code
Do Ngoc Anh
Member
Code
Do Hoang Nam
Member
Code

## Slide 3: ASSIGN WORK
2. Nguyen Duc Tung
1. Tran Dinh Bien
Implement User communicationmain part, main part, GPIO.
General management of progress and implementation work
3. Do Ngoc Anh
Implement Flash part, bootloader function, slide and present.
Design and build up application of read temperature from on-boad sensor, send 10 latest value to pc for each received command of 0x55
4. Do Hoang Nam
Implement UART receive File, Parse File Srec.

## Slide 4: Light bulb of contents
.srec
Our idea
IRL
Bootloader
Memory layout
Flowchart
SREC file

## Slide 5: About Bootloader
01
So, what are we talking about ?

## Slide 6: What is Bootloader ?
Bootloader is a special software that is loaded into the computer’s memory before booting.
If there is a Bootloader program loaded into the microcontroller, it will first jump into this Bootloader program, do some work and then switch to the application program to execute.
Application
Bootloader
…

## Slide 7: So, why do we need Bootloader ?
Update Firmware
Enable to update wirelessly without going to store to reload the Firmware
Security
Can insert some code to check if the loaded Firmware is correct or not. If not valid, the update will not be allowed

## Slide 8: Our idea 02
Which option did we choose ?

## Slide 9: Board : MKE16Z64 of NXP Chip : ARM Cortex M0+ Software: MCUXpresso IDE Hercules
Hardware & Software

## Slide 10: Firmware
Run Current App
Default : Blink LED
App 1 : Read Temperature Sensor
App 2 : Control LED with button
Application Mode
Execute User command
Add new App
Erase old App
Load selected App
Bootloader Mode

## Slide 11: Memory layout
03
Where to store code & data ?

## Slide 12: MKE16Z64 memory layout 01 02
Used to store program code and commands ( MSP, Vector Table … )
Flash memory
This device contains 1 block (64 KB) of program flash consisting of 1 KB sectors starting at address 0x0000_0000
SRAM memory
Used to store temporary data during run-time
The on-chip SRAM is split into SRAM_L and SRAM_U regions anchored at address 0x2000_0000
SRAM_L size : 2 KB
SRAM_U size : 6 KB
- Divided into 64 sectors
- Write in Word (4 bytes)
- Erase by Sector

## Slide 13: SREC file
Structure & Style
04

## Slide 14: SREC file structure
S19-style 16-bit address records
Data
Header
End

## Slide 15: Flowcharts
Easy to follow
05

## Slide 16: Main flowchart
Reset
Jump to address 0x0000_0000
Main() function
SW3 is held ?
Bootloader Mode
Add / Erase / Load ?
Application Mode
Jump to Current App
Application code
Soft Reset
T
F
Super Loop

## Slide 17: Bootloader Mode flowchart
Start
Receive Command via UART
Command valid ?
Add ?
Receive SREC file via UART
Write to Flash
F
T
Erase ?
Erase the sector containing Erasing App
Load ?
Set Current_App_Address = Loaded_App_Address
T
T
Reset
End

## Slide 18: Parse SREC file flowchart

## Slide 19: Flash command write sequence flowchart

## Slide 20: Bootloader() function flowchart
Get address to jump to
Disable all interrupts
Start
Set SCB->VTOR
Set Main Stack Pointer
Set Program Counter
Jump to App
SCB->VTOR = APP_START_ADDRESS;
__set_MSP(*((volatile u32*) APP_START_ADDRESS);
pFunction_t JumptoApp = (pFunction_t)(*((volatile u32*)(APP_START_ADDRESS + 4)));
JumptoApp();
APP_START_ADDRESS = Current_App_Address
__disable_irq();
SysTick->CTRL = 0;
End

## Slide 21: Application flowchart

## Slide 22
Configure ADC module
  Input clock = 1 MHz
  Internal clock ADC = 1/8 MHz
  ADC resolution = 10 bit
  ADC channel = temp sensor channel
Note
  m is the hot or cold voltage versus temperature slope in V/°C
  Vtemp is the voltage of the temperature sensor channel at the ambient temperature
  Vtemp25 is the voltage of the temperature sensor channel at 25°C and VDD = 3 V

## Slide 23: Calculation example
Vtemp = Vtemp * 0.003125 ; // Convert the ADC reading into voltage if (Vtemp => 0.7012) // Check for Hot or Cold Slope
{ Temp1 = 25 – ((Vtemp – 0.7012) / 0.001646); // Cold Slope }
else
{ Temp1 = 25 – ((Vtemp – 0.7012) / 0.001749); //Hot Slope
}
Note: VDD = 3.2 volts for the VTEMP conversion

## Slide 24: IRL
06
Let’s him cook !!!

## Slide 25: Resources
Here’s the reference resources for this project:
Bootloader: https://www.laptrinhdientu.com/2021/10/Bootloader1.html
Board KE16: KE16’s Reference Manual
SREC file: https://en.wikipedia.org/wiki/SREC_(file_format)
Special thanks to our teacher:
Nguyen Van Nghia

## Slide 26: Thanks!
Do you have any questions?
Muốn nắm chắc kiến thức thì phải học Vậy học như nào để nắm được tay em :(((